## Slide 1: Internet Key Exchange
RFC 2409/4306
Nathan Bellew

## Slide 2: Overview
History of IKE
Why IKE is used
What is IKE
  IKE Phases
  Mode of Operation
  Authentication Methods
  Session Keys
  ISAKMP/IKE

## Slide 3: History of IKE
Internet Security Association and Key Management (ISAKMP)
  Security Framework
IPSec
  IP Security
Diffie-Hellman
  Authentication
Photuris
  Key Security
Oakley
  Secure Key Exchange
Secure Key Exchange Mechanism (SKEME)
Internet Key Exchange
  Secure Key Exchange

## Slide 4: Why IKE
ISAKMP -> Authentication and Key Exchange Framework
Oakley -> Key Exchange Modes
SKEME -> anonymity, reputability, and key refreshment
Each is good but we needed All!
ISAKMP
SKEME
Oakley
Internet Key Exchange

## Slide 5: IKE Phases
Only 2 Phases?
Phase 1: Mutual Authenticaiton and Session Keys = IKE SA
Phase 2: Create Multiple Associations between entities = ESP or AH SA
IKE – Internet Key Exchange
SA – Security Association
ESP – Encapsulating Security Payload
AH – Authentication Header

## Slide 6: Modes of Phase 1
Main Mode
  6 Messages
Aggressive Mode
  3 Messages

## Slide 7: IKE Authentication Methods
Public Key Signature
Original Public Key Encryption
Revised Public Key Encryption
Pre-shared secret Key

## Slide 8: Phase 1 Steps
Choose a Mode
  Aggressive or Main
Authenticate and Protect IPSec Peers
Create Shared Secret Keys (Diffie-Hellman) and Cookies (ISAKMP)
Establish secure tunnel for Phase 2 Parameters

## Slide 9: Key Determination - Cookies
Anti Clogging Technology
Preps Diffie-Hellman
Anti-Replay Technology
Stops Man from being in Middle
The Cookie Exchange

## Slide 10: Key Determination – Diffie Hellman
Oakley Key Determination
Secret Session Key 
Group Identifiers RFC 2412
Oakley First Default Group
=2

## Slide 11: Session Keys
SKEYID = hash (DH values, nonces, cookies, etc.) Key Seeds
Phase 1 - SKEYID last message
Phase 2 – SKEYID all Messages
Pseudo Random Function (prf) -with two parameters key and data (Think DES CBC or HMAC)

## Slide 12: IKE Phase 2
Quick Mode – Negotiation and Nonce Exchange
IPsec (AH or ESP) SA – Crypto Parameters and Traffic Selectors
Traffic Selectors – IP address/mask, IP protocol type and port

## Slide 13: IKE Phase 2 Cont.
X = pair of cookies from Phase 1
Y = 32 bit number to distinguish phase 2 sessions
CP – Crypto Proposal, CPA – Accepted proposal
SPI (from ISAKMP) – Security Parameter Index – IP SA Details
Nonce – random number
Diffie Hellman (optional) – For PFS

## Slide 14: Header Formats

## Slide 15: IKEv2 The New One
RFC 4306 – Goodreads rating 9.5/10
Replaced RFCs 2407, 2408, 2409
Simplifies Key Exchange
Easier to implement
Less vulnerable to DoS

## Slide 16: Summary
IKE Is really cool
IKE is made from ISAKMP, SKEME, and Oakley protocol
IKE consists of 2 phases
  Big connection from A to B
  Small connections from each node from A to B
Aggressive and Main – For IKEv1 but not for IKEv2
IKEv2 made this whole thing way easier
Reading RFCs for fun is really cool.